## Slide 1: Aqua Permit Simulations: Foster, Tiner, and Waterson 1 and 2
Draft Report: June 2, 2023
Supplemental Information: November 8 and November 11, 2023
William R. Hutchison, Ph.D., P.E., P.G.
November 15, 2023

## Slide 2: Summary Well Data

## Slide 3: Aquifer Completion Data

## Slide 4: Aquifer Completion Data

## Slide 5: Simulation Summary (Foster)
Proposed pumping volume = 807 AF/yr
Drawdown from 2011 to 2070 at Foster Well location = 18 ft
Significant sources of the proposed pumping:
  Captured outflow that would have gone to Caldwell and Fayette counties.
  Vertical inflow from the overlying Reklaw formation
  Storage reduction in the Carrizo Aquifer.

## Slide 6: Simulation Summary (Tiner)
Proposed pumping volume = 4,839 AF/yr
Drawdown from 2011 to 2070 at Tiner Well location = 102 ft
Significant sources of the proposed pumping:
  Induced inflow from the shallow flow system.
  Induced vertical inflow from the overlying Reklaw formation.
  Storage reduction in the Carrizo Aquifer.
  Captured outflow components from Fayette County
  Captured vertical outflow to the underlying Calvert Bluff Aquifer
  Storage decline in the Carrizo Aquifer.

## Slide 7: Simulation Summary (Waterson 1)
Proposed pumping volume = 3,226 AF/yr
Drawdown from 2011 to 2070 at Waterson 1 well location = 119 ft
Significant sources of the proposed pumping:
  Over half of the proposed pumping would be sourced as induced inflow from the shallow flow system.
  Induced inflow from the overlying Carrizo Aquifer.
  Storage decline supplies less than ten percent of the increased pumping.

## Slide 8: Simulation Summary (Waterson 2)
Proposed pumping volume = 3,226 AF/yr
Drawdown from 2011 to 2070 at Waterson 2 well location = 163 ft
Significant sources of the proposed pumping:
  Over half of the proposed pumping would be sourced as induced inflow from the shallow flow system.
  Induced inflow from the overlying Carrizo Aquifer.
  Storage decline supplies less than ten percent of the increased pumping

## Slide 9: Attributable Drawdown Hydrographs
Foster
Tiner
Waterson 1
Waterson 2

## Slide 10: Attributable Drawdown (Foster)

## Slide 11: Attributable Drawdown (Tiner)

## Slide 12: Attributable Drawdown (Waterson 1)

## Slide 13: Attributable Drawdown (Waterson 2)

## Slide 14: Groundwater Budget Results
Foster
Tiner
Waterson 1
Waterson 2

## Slide 15: Groundwater Budget (Foster)

## Slide 16: Groundwater Budget (Tiner)

## Slide 17: Groundwater Budget (Waterson 1)

## Slide 18: Groundwater Budget (Waterson 2)

## Slide 19: Analysis of Nearby Wells

## Slide 20: Distance-Drawdown Graphs
Foster
Tiner
Waterson 1
Waterson 2

## Slide 25: Attributable Drawdown Contours
Foster
  Layer 7
Tiner
  Layer 7
  Layer 6
  Layer 8
  Layer 2
Waterson 1
  Layer 9
  Layer 8
  Layer 10
  Layer 2
Waterson 2
  Layer 9

## Slide 26
Foster – Layer 7

## Slide 27
Tiner – Layer 7

## Slide 28
Tiner – Layer 6

## Slide 29
Tiner – Layer 8

## Slide 30
Tiner – Layer 2

## Slide 31
Waterson 1 – Layer 9

## Slide 32
Waterson 1 – Layer 8

## Slide 33
Waterson 1 – Layer 10

## Slide 34
Waterson 1 – Layer 2

## Slide 35
Waterson 2 – Layer 9